## Slide 1
AMBULATORY AND VIDEO EEG
Amar B. Bhatt, MD, FAES
Assistant Professor of Neurology, Epilepsy Section
Rush University Medical Center

## Slide 2
DISCLOSURES
Disclosure of Financial Relationships
None
Off-Label Usage
  None

## Slide 3: Objectives
Uses of video-EEG monitoring
Options for EEG monitoring
Yield of EEG monitoring
Activation procedures used to increase yield
Comparison of different types of EEG monitoring

## Slide 4: Uses of Video-EEG monitoring
Diagnosis (epileptic vs. non-epileptic)
Interictal Epileptiform Discharges
Classification and Localization
Medication Adjustment
Seizure / Discharge Quantification
Surgical Candidacy Evaluation

## Slide 5: Options for EEG monitoring
Short-term – inpatient or outpatient
  Routine video-EEG (20-60 min)
  Prolonged/Extended video-EEG (1-4 hours)
Long-term – outpatient
  Ambulatory EEG
  Home video-EEG – a growing trend
Long-term – inpatient
  Portable continuous video-EEG (usu. ICU) – a.k.a. cEEG*
  Hard-wired continuous video-EEG (usu. Epilepsy Monitoring Unit) – a.k.a. EMU*
*some ICUs are hard-wired, some EMUs are portable

## Slide 6
What is the typical yield of a routine outpatient EEG study in adults? (chance of capturing an epileptiform abnormality in a patient with suspected epilepsy)
25%
33%
50%
66%
80%
Notes: C is the correct answer. A single routine EEG has a yield of about 40-50%, and multiple repeat studies or prolonged outpatient studies, may increase the yield to 80-90%. At that point, repeat EEGs do not increase the yield, and long-term monitoring should be considered (continuous EEG monitoring, ambulatory EEG, or epilepsy monitoring unit admission).

## Slide 7: Methods of increasing EEG Yield
Single routine EEG: 40-50% yield* in epileptic patients
Repeat and 2-4 hour extended EEGs increase yield* to 80-90%
Remaining Cases: Long-term monitoring (cEEG, EMU, Ambulatory EEG)
*this yield is for interictal epileptiform discharges (not diagnostic of epilepsy)

## Slide 8: Activating Procedures
Hyperventilation and Photic Stimulation
  Mostly for generalized epilepsies
  Lack of slow activity or driving still normal
Drowsiness and Sleep

## Slide 9: Harmonic driving
Driving response that is a multiple or factor of the flash frequency
Can be half, double, triple, etc.
Can have a “notched” appearance (multiple fused frequencies)

## Slide 10
Notes: double

## Slide 11
Peaks at 9, 18, and 27 Hz

## Slide 12
Which of the following responses is abnormal during photic stimulation?
Photoconvulsive response
Photomyogenic response
Photomyoclonic response
Photovoltaic response
Photocell response
Notes: A is the correct answer. Photoconvulsive response is also known as photoparxoysmal response. Although some controversy exists as to nuanced differences between these two terms, both require generalized (usually frontally or occipitally predominant) spike-and-wave discharges during photic stimulation, which are consistent with generalized epileptogenicity, though not necessarily diagnostic of generalized epilepsy. Photomyogenic and photomyoclonic response both refer to a benign frontalis muscle contraction that occurs time locked with the photic flash. Photocell or photovoltaic response is an artifact in which a high impedance electrode creates a “cell” or “battery” capable of storing charge, which is released with each photic flash, resulting in a time locked spiky response on EEG, but only specifically in the electrode with the high impedance.

## Slide 13: Photoparoxysmal response
a.k.a. photoconvulsive response*
Assoc. with generalized epilepsy
  Usu. generalized / bifrontally predominant
  May be bioccipitally predominant
  May have assoc. absence, myoclonic, or generalized tonic clonic (GTC) seizures
Assoc. with occipital epilepsy if unilateral (rare)
*controversial: some say photoconvulsive implies that discharges outlast the flash
Notes: Although some controversy exists as to nuanced differences between these two terms, both require generalized (usually frontally or occipitally predominant) spike-and-wave discharges during photic stimulation, which are consistent with generalized epileptogenicity, though not necessarily diagnostic of generalized epilepsy.

## Slide 16: Photomyogenic response
a.k.a. photomyoclonic response
this is benign
don’t let “myoclonic” fool you
EMG potentials (frontal) time-locked to the flash frequency

## Slide 18: Photovoltaic (photocell) artifact
high impedance electrode creates a “cell” or “battery” capable of storing charge
released with each photic flash, resulting in a time locked spiky response on EEG
only specifically in the electrode with the high impedance.

## Slide 22
Normal impedance:
0.1 to 5 kOhms
(100 – 5000 𝛀)

## Slide 23: Ambulatory EEG
Home-based EEG recording
May have a daily patient visit to fix electrodes and download data
Patient must push button or record in diary
Cheaper and more widely available than EMU

## Slide 24: Ambulatory EEG – Uses
Event capture – yield is 40-70%
Interictal yield – 48 hours captures 95% of such patients
Nocturnal disorders (frontal seizures, sleep disorders, ESES/CSWS)
Quantifying subclinical / subtle clinical seizures
Determining recurrence risk when considering seizure medication withdrawal
Faulkner et al, Clin Neurophysiol, 2012; Lawley et al, Epilepsy and Behavior, 2015

## Slide 25: Ambulatory EEG
Advantages
  minimal interference with patient activities
  natural environment to trigger events/seizures
Disadvantages
  prone to artifacts
  no video or real-time monitoring (in most cases)
  cannot examine patient during event
  cannot safely withdraw medications

## Slide 26: Importance of Video
Semiology analysis
Correlation to patient / witness history
Assessment for artifact
Diagnosis (esp. when EEG is normal)

## Slide 27: Long-term video-EEG monitoring
EMU remains the diagnostic “gold” standard
Ideally requires:
  Ictal EEG, video, and exam
  Interictal EEG recording with med withdrawal
  Correlation to history (confirm all of patient’s full blown and typical event types were captured)

## Slide 28: Long-term video-EEG monitoring
Advantages
  invasive monitoring
  ictal functional imaging
  medication adjustment
Disadvantages
  high cost (techs, nursing, physicians, hospital)
  disrupts patient’s normal activities and work/school
  risk of nosocomial infections
  risk of physical and psychological harm/injury

## Slide 29: Refer refractory cases!
Why?
  To confirm diagnosis of epilepsy
  For alternative treatment options (surgery, etc.)
  To avoid inappropriate treatments
What defines refractory?
  Lack of seizure control with two properly dosed medications
  NOT failed due to side effects

## Slide 30
A 28-year-old man develops new onset partial seizures. Treatment with levetiracetam is initiated, and the dose is titrated up to 1500 mg twice daily without seizure recurrence. However, he does not tolerate this medication due to worsening depression. The medication is tapered off and lamotrigine is titrated upward. What is the patient’s chance of seizure freedom with lamotrigine?
~75%
~66%
~50%
~33%
~15%
Notes: C is the correct answer. Based on the landmark Kwan and Brodie study (NEJM, 2000), about 47% of patients will become seizure free with the first medication and about 13% will become seizure free with the second medication. However, in this case, the first medication (levetiracetam) does not count as a failure, since it was discontinued due to side effects, and not due to lack of seizure control. Overall, after trying multiple (at least 2-3) medications, about 66% of patients with epilepsy will become seizure free.

## Slide 31: Chances of Seizure Freedom
Kwan and Brodie, NEJM, 2000.
Chen, Brodie, Liew, and Kwan, JAMA Neurology, 2018.
Seizure-free with surgery (in the right cases): up to 70%
Chart: 
| first drug | second drug | third drug | multiple drugs | refractory
 | 222 | 61 | 6 | 12 | 169
 | 0.47234 | 0.12979 | 0.012766 | 0.025532 | 0.35957

## Slide 32
In a patient with epilepsy, how many medications should be failed due to lack of seizure control prior to considering referral to an epilepsy center (or epilepsy monitoring unit)?
One
Two
Three
Four
Five
Notes: B is the correct answer. The definition of medically refractory epilepsy is failure of seizure control after two appropriately doses seizure medications (not failed due to side effects). Although a third or fourth medication may be considered, the chance of seizure freedom is quite low after the second medication. At that point, the physician must consider an alternate diagnosis (e.g., non-epileptic events) or alternate treatments (e.g., epilepsy surgery).

## Slide 33: Unnecessary VNS in PNES
60 consecutive VNS patients in EMU
13 had PNES exclusively (none had prior EMU)
  all on 2-4 medications
  all discharged off medications
  duration of VNS therapy: 0.5 – 5 yrs
  mean latency to PNES diagnosis: 2.8 yrs
Over-interpretation of outpatient EEGs?
Arain et al, Epilepsy and Behavior, 2011

## Slide 34: Diagnostic usefulness and duration of the inpatient long-term video-EEG monitoring
234 consecutive LTM studies over 2 yrs (221 patients)
Diagnostically useful in 44% (typical event previously not captured)
  Not different between age groups
  Not different between referral groups [diagnostic (41%), classification (41%) and presurgical (55%)]
Duration of successful LTM significantly longer in the presurgical group (mean: 3.5 days) vs. diagnostic and classification groups (2.4 and 2.3 days, respectively)
Alving and Beniczky, Seizure, 2009
courtesy of Dr. Abou-Khalil
Notes: Diagnostically useful defined as: at least one ictal episode that matched the patients’ habitual events but which had not been
sufficiently documented during previous investigations (short-term video-EEG monitoring or clinical observation/video-recording)

## Slide 35
What is the typical diagnostic yield (chance of capturing a patient’s typical events) during epilepsy monitoring unit (EMU) admission?
20-25%
40-45%
60-65%
80-85%
90-95%
Notes: D is the correct answer. Two well-designed independent studies of large cohorts have found similar results, in that about 80-85% of patients will be definitively diagnosed during their first EMU admission. Among those patients being re-admitted for monitoring due to have a non-diagnostic first study, the yield is about 40-50% the second time around.

## Slide 36: Non-diagnostic EMU studies
Diagnostic yield of 1st EMU study: 82-85%
Diagnostic yield of 2nd EMU study: 42-53%
Factors associated with non-diagnostic study:
  younger age (in adults)
  longer duration of monitoring
  normal outpatient EEG
  absence of epilepsy risk factors
Elgavish and Cabaniss, J Clin Neurophysiol, 2011: ~3600 patients
Robinson et al, Epilepsy and Behavior, 2011: ~2400 patients
Notes: 87 and 43 had a repeat study
2nd study used 150 controls for the nondiagnostic patients: odds of successful study increased 1.6 times for each epilepsy risk factor
Two well-designed independent studies of large cohorts have found similar results, in that about 80-85% of patients will be definitively diagnosed during their first EMU admission.
Among those patients being re-admitted for monitoring due to have a non-diagnostic first study, the yield is about 40-50% the second time around.

## Slide 37: Co-existent epilepsy and PNES
Occurrence has “decreased” historically
  possibly due to wider use of video-EEG monitoring
  estimated to be 5-15%
Key factors in successful monitoring
  duration (5 days suggested as optimal*)
  Seizure medication withdrawal
  capture of all typical event types
*Foong and Seneviratne, J Clin Neurosci, 2016

## Slide 38
Non-convulsive seizures / status epilepticus have a typical combined incidence of 20-25%
May vary (8-48%) depending on the study
40-92% of seizures on cEEG are nonconvulsive
Continuous EEG (cEEG) in the ICU

## Slide 39: NCS/NCSE: When to consider cEEG
Altered mental status (esp. unexplained)
History of epilepsy or recent seizures (esp. GTCS)
Subtle twitching, eye deviation, nystagmus
Recent CNS procedure, infections, stroke, neoplasms (esp. when pt is worse than expected)
Chronic focal cortical injury
Notes: Prolonged post-ictal state – 50% chance of NCS
Patients with a preadmission diagnosis of epilepsy or recent seizures
It is clear that unless we are continously monitoring every patient with AMS in the ICU, we are likely missing a lot of NCSs
All NCS/NCSE is not the same but there is no consensus classification scheme - Based on review of the literature

## Slide 40
In critically ill, non-comatose patients undergoing continuous EEG monitoring, what duration of monitoring is recommended to capture a seizure in the majority (95%) of patients who will develop seizures in the ICU?
1 hour
6 hours
12 hours
24 hours
48 hours
Notes: D is the correct answer. Based on the landmark paper by Claassen et al. (Neurology, 2004), of critically ill patients who are found to have nonconvulsive seizures on continuous EEG, 95% of the non-comatose patients will have their first seizure by 24 hours, and 87% of the comatose patients will have their first seizure by 48 hours. Longer monitoring can always be considered, but to have reasonable resource utilization and cost-effectiveness, 24 hours of monitoring of non-comatose patients (and 48 hours of monitoring of comatose patients) is a reasonable guideline, particularly if the EEG does not show any epileptiform discharges or rhythmic/periodic patterns that may warrant longer monitoring.

## Slide 41: Continuous EEG in critically ill patients
    570 patients with altered mental status
Longer cEEG duration required in comatose patients
To capture most seizures:
Noncomatose  24 hrs
Comatose  48 hrs
Claassen et al., Neurology 2004;62:1743–8.
Notes:     Retrospective study - 19% had seizures detected - 92% of these were nonconvulsive
      Epilepsy related seizures (33%)
      CNS infection (29%)
      Brain Tumor (23%)
      After neurosurgical intervention (23%)

## Slide 42
 | Routine EEG | Extended EEG | Continuous portable EEG | Long-term EEG (EMU) | Ambulatory EEG | Home vEEG
Availability | + | + | - | - | + | --
Duration | -- | - | ++ | ++ | + | +
Video | + | + | + | + | - | +
Ictal EEG | -- | - | + | ++ | + | +
Examination | + | + | - | ++ | -- | --
EEG quality | + | + | + | ++ | - | +
Surgery | - | - | + | ++ | - | -
Natural environment | - | - | - | - | + | +
Acute use | + | + | ++ | + | -- | --
Med change | - | - | + | ++ | - | -
Hx correlate | - | - | + | ++ | - | -
Quantify sz | - | + | ++ | ++ | + | +
Sleep EEG | - | + | ++ | ++ | ++ | ++
HV/Photic | + | + | + | + | - | -
Affordability | ++ | + | -- | -- | + | -

## Slide 43: References
Alving J, Beniczky S. Diagnostic usefulness and duration of the inpatient long-term video-EEG monitoring: findings in patients extensively investigated before the monitoring. Seizure. 2009 Sep;18(7):470-3. doi: 10.1016/j.seizure.2009.04.005. Epub 2009 May 9. PubMed PMID: 19428271
Arain AM, Song Y, Bangalore-Vittal N, Ali S, Jabeen S, Azar NJ. Long term video/EEG prevents unnecessary vagus nerve stimulator implantation in patients with psychogenic nonepileptic seizures. Epilepsy Behav. 2011 Aug;21(4):364-6.
Cascino GD. Video-EEG monitoring in adults. Epilepsia. 2002;43 Suppl 3:80-93. Review. PubMed PMID: 12060010.
Chen Z, Brodie MJ, Liew D, Kwan P. Treatment outcomes in patients with newly diagnosed epilepsy treated with established and new antiepileptic drugs: a 30-year longitudinal cohort study. JAMA neurology. 2018 Mar 1;75(3):279-86.
Claassen J, Mayer SA, Kowalski RG, Emerson RG, Hirsch LJ. Detection of electrographic seizures with continuous EEG monitoring in critically ill patients. Neurology. 2004 May 25;62(10):1743-8. Review. PubMed PMID: 15159471.
Elgavish RA, Cabaniss WW. What is the diagnostic value of repeating a nondiagnostic video-EEG study? J Clin Neurophysiol. 2011 Jun;28(3):311-3. doi: 10.1097/WNP.0b013e31821c3aa9. PubMed PMID: 21633258.
Faulkner HJ, Arima H, Mohamed A. Latency to first interictal epileptiform discharge in epilepsy with outpatient ambulatory EEG. Clin Neurophysiol.2012-123(9):1732-1735. doi:10.1016/.clinph.2012.01.023
Foong M, Seneviratne U. Optimal duration of video-electroencephalographic monitoring to capture seizures. J Clin Neurosci. 2016 Jun;28:55-60. doi: 10.1016/j.jocn.2015.10.032. Epub 2016 Mar 5. PubMed PMID: 26960265.
Khan OI, Azevedo CJ, Hartshorn AL, Montanye JT, Gonzalez JC, Natola MA, Surgenor SD, Morse RP, Nordgren RE, Bujarski KA, Holmes GL, Jobst BC, Scott RC, Thadani VM. A comparison of continuous video-EEG monitoring and 30-minute EEG in an ICU. Epileptic Disord. 2014 Dec;16(4):439-48. doi: 10.1684/epd.2014.0715. PubMed PMID: 25498516.
Kwan P, Brodie MJ. Early identification of refractory epilepsy. N Engl J Med. 2000 Feb 3;342(5):314-9.
Lawley A, Evans S, Manfredonia F, Cavanna AE. The role of outpatient ambulatory electroencephalography in the diagnosis and management of adults with epilepsy or nonepileptic attack disorder: A systematic literature review. Epilepsy Behav. 2015 Dec;53:26-30. doi: 10.1016/j.yebeh.2015.09.032. Epub 2015 Oct 26. Review. PubMed PMID: 26515156.
Modur PN, Rigdon B. Diagnostic yield of sequential routine EEG and extended outpatient video-EEG monitoring. Clin Neurophysiol. 2008 Jan;119(1):190-6. Epub 2007 Nov 26. PubMed PMID: 18042424.
Ney JP, van der Goes DN, Nuwer MR, Nelson L, Eccher MA. Continuous and routine EEG in intensive care: utilization and outcomes, United States 2005-2009. Neurology. 2013 Dec 3;81(23):2002-8. doi: 10.1212/01.wnl.0000436948.93399.2a. Epub 2013 Nov 1. PubMed PMID: 24186910; PubMed Central PMCID: PMC3854828.
Robinson AA, Pitiyanuvath N, Abou-Khalil BW, Wang L, Shi Y, Azar NJ. Predictors of a nondiagnostic epilepsy monitoring study and yield of repeat study. Epilepsy Behav. 2011 May;21(1):76-9. doi: 10.1016/j.yebeh.2011.03.014. Epub 2011 Apr 19. PubMed PMID: 21507729.
Shafi MM, Westover MB, Cole AJ, Kilbride RD, Hoch DB, Cash SS. Absence of early epileptiform abnormalities predicts lack of seizures on continuous EEG. Neurology. 2012 Oct 23;79(17):1796-801. doi: 10.1212/WNL.0b013e3182703fbc. Epub 2012 Oct 10. PubMed PMID: 23054233; PubMed Central PMCID: PMC3475619.
Vespa PM, Nenov V, Nuwer MR. Continuous EEG monitoring in the intensive care unit: early findings and clinical efficacy. J Clin Neurophysiol. 1999 Jan;16(1):1-13. PubMed PMID: 10082088.